## Slide 1
Driver Verification Using Eye Movements and Blinking
Azhar Quddus, Ph.D.
Ali Zandi, Ph.D.
Laura Prest
Felix Comeau
CARSP ACPSER Conference 2018

## Slide 2
  Need to authenticate driver identity from safety point of view:
    Verification of people operating in-vehicle safety devices, e.g. alcohol interlocks
    Identification of drivers in connected vehicles
    Self-driving mode
  Various technologies available for identification/verification of people
  Many are not robust against circumvention/spoofing and/or or interfere with the driver activity
Background
https://internationalbanker.com/banking/putting-right-finger-forward-consumer-technologies-encouraging-biometric-banking/
http://transportationtech.com/qualcomm-unveils-next-gen-connected-vehicle-chipset/
acs-corp.com

## Slide 3
An international group of companies (beginning in 1970) with a Canadian headquarter
Pioneer in alcohol detection technology and road safety
Scientific research, product development, and manufacturing
Alcohol Countermeasure System Corp. (ACS)
Research collaborations with academic sector
In-house R & D

## Slide 4
To develop non-intrusive real-time techniques for reliable and practical identification/verification of the driver, using eye movements and blinking.
Objective

## Slide 5: Methods
  Simulated Driving Task (SDT)
    More real-world situation using a driving simulator
    Two separate sessions (different conditions & time of the day):
      10-min control driving (CD)
      30-min monotonous driving (MD)
    30 subjects (age 40.13±9.69 years; 8 females)
    Alcohol Countermeasure System Corp., Toronto, Canada
    Smart Eye Pro system (60 Hz; two IR-based cameras)
SmartEye Pro Eye Tracker

## Slide 6
Methods
General Gaze | Average, median, standard deviation, duration, frequency, percentage, scanpath, velocity, similarity index
Fixation | 
Saccade | 
Blinking | 
  Classification:
    Non-linear support vector machine (SVM) with RBF kernel
    Gradient boosted tree (GBT) with maximum depth of 5
  Evaluation:
    CD alone
    MD alone
    Mixed CD and MD
  Feature Extraction (28 features):
    10-sec window with 50% overlap

## Slide 7
Methods
Feature extraction (Left), Training (Middle), Verification (Right)
Feature vectors
(training set)
SVM classifier
GBT classifier
Eye tracking data
timing window (10 sec)
Time
Feature vectors
Feature vectors
(testing)
SVM classifier
GBT classifier
Fusion
Models
Fused score
Training
Testing

## Slide 8
Results
CD Session:

## Slide 9
Results
MD Session:

## Slide 10
Results
Mixed Sessions:

## Slide 11
  A machine learning based approach for driver verification using eye tracking data.
  A simulated driving task (SDT).
  The proposed methodology is suitable for practical implementation using simple features extracted in real-time.
  The verification scheme can be easily implemented on embedded platforms.
  Next steps:
  Real driving conditions
  Larger number of subjects
  Other AI technologies including deep learning techniques
  Extension to identification
Conclusion & Discussion

## Slide 12
Ali Zandi, Ph.D.
aszandi@acs-corp.com
Azhar Quddus, Ph.D.
aquddus@acs-corp.com
Thank you!
Q & A